TFT ESP32 Notes

Extended UTFT library

Modified version to use ESP32 in 8-bit parallel mode. Direct ESP32 register control for interface.

Additional graphical functions:

Original circle fill was inaccurate, replaced.

Original three byte R,G,B 24-bit colour conversion to 16 bit inaccurate, replaced with fixed point calculation.

Added Ellipse draw and fill.

Added Triangle draw and fill

Added 4-point Bezier curve using fixed point calculations for speed.

Added 1-bit bitmap icon handling with background mask option.

Added 4-bit bitmap icon handling with background mask option.

Additional Applications

Two windows applications were produced in support of the new UTFT library,
1. image_convert1.exe
     This application is used to convert the 1 of 4 bit bitmaps to a .h file to produce to icon in the
      Adruino software for the TFT display.
2. PalletEdit.exe
    This application is used to edit the 16 colour pallet table in the 4-bit bitmap to produce a range of colours matching those used in 24-bit bitmap icons.

4-bit Bitmap icon handling

It was found that when 24-bit bitmaps were used to produce icons, it was rare to use more than 16 colours. Thus by editing the 16 colour pallet table using the PalletEdit.exe application, those colours could be reproduced using the 4-bit bitmap.

Example; a 64x64 24 bit bitmap icon of a rain gauge 12,342 bytes

Now a 64x64 4-bit bitmap icon with edited pallet table 2,166 bytes